The files 'SAVBAT.EXE' and 'SAVBATTI.EXE' are executables that can be included
for use in the 'AUTOEXEC.BAT' file.  These routines (SAVBAT = IBM, SAVBATTI =
TIPC) configure the parallel port that the PCIF is attached to for minimal
power consumption from the calculator batteries if the PCIF is to be left
attached to the PC for long periods of time.  After a 'boot' on the PC, the
port will be in a state where the calculator batteries are being drained at
a significant level.  By running the SAVBAT software, the port will be placed
in a state where the calculator batteries are not drained at this level, but at
a much lower level.  The port is left in this same state when the 'PCIF'
software is exited.  By including a line 'SAVBAT' in your AUTOEXEC.BAT file,
the port will be properly configured everytime you re-boot the PC.

For the IBM compatible version, specify SAVBAT /0, SAVBAT /1, or SAVBAT /2,
depending on the parallel port used for the PCIF.

  /0  : primary parallel port at address 378H
  /1  : secondary parallel port at 278H
  /2  : parallel port at address 3BCH

For the TIPC version, copy the SAVBATTI.EXE file to your system for use.
No parameters are required for the TIPC version.