NEW TEP  Andy Cooper's fast new version of TE-p emulates a VT52
              terminal at speeds up to 9600 baud (4800 if continuous high
     -speed scrolling is needed.  This version also supports 40 column
     windowing in an 80 column screen buffer using the conventional TI
     P-system function keys.  The Xmodem transfer routine has been modified
     to allow transfers of large files up to the limit of your disk
     capacity.  P-system users are indebted to Andy for this significant
     refinement of his outstanding communication program for the P-system.
     The documentation below comes from correspondence with Andy during the
     development of this program and supplements Andy's original TE-p docs.
 
     Escape Sequences    Action 
        
         ESC A           Cursor UP 
         ESC B           Cursor DOWN 
         ESC C           Cursor FORWARD 
         ESC D           Cursor BACKWARD 
         ESC E           Clear display 
         ESC H           Cursor home 
         ESC I           Reverse Index 
         ESC J           Erase to end-of-screen 
         ESC K           Erase to end-of-line 
         ESC L           Insert line 
         ESC M           Delete line 
         ESC Y ...       Direct cursor addressing 
 
     Control Sequences 
      
     With few exceptions the CTRL combinations are the standard ones used
     in the P-system keyscan, i.e., CTRL a through CTRL z send ASCII
     characters 01 through 26 (SOH through SUB).  The exceptions are: 
      
        CTRL  <space> or <@>  -------------> NUL (ASCII 00) 
        CTRL    <;>    --------------------> ESC (ASCII 27) 
        CTRL    <<>    --------------------> FS  (ASCII 28) 
        CTRL    <=>    --------------------> GS  (ASCII 29) 
        CTRL    <>>    --------------------> RS  (ASCII 30) 
        CTRL           (control key alone)-> US  (ASCII 31) 
      
     In normal ASCII communication mode (not XMODEM) TE-p responds only to
     the ASCII control codes for backspace, linefeed, and carriage return. 
      
     Special Control and Function Keys 
      
        CTRL 1           Change screen color 
        CTRL 2         * Print screen 
        CTRL 3           Change cursor (underscore/block) 
        CTRL 4           40/80 column mode (Default = 40) 
        CTRL 5           Xmodem Transmit 
        CTRL 6           Xmodem Receive 
      
        FCTN 7           Window Left (80 col mode only) 
        FCTN 8           Window Right (80 col mode only) 
        FCTN 9           Abort Xmodem transfer 
        FCTN =           Exit from TE-p 
      
        FCTN <s> or <S>  Transmit DEL (ASCII 127) 
      
     * will hang if PIO or printer off
                                           6-07-86 Jerry Coffey [74716,3525]
`