CALL IOX

          =================================================================
           
                     /(device, command [, status-variable])\
          CALL IOX {                                         }
                     \(string-variable [, status-variable]) /
           
          =================================================================
          The IOX subprogram is an extended version of  the  IO  subprogram
          built  into  the  TI-74.   It performs special control operations
          which are not available in the TI-74 BASIC, but may be  supported
          by  some  peripherals.   Proper  use  of this subprogram requires
          knowledge of input/output  (I/O)  data  structures  and  specific
          peripheral capabilities. Refer to the peripheral manuals for more
          information regarding these capabilities.

               'Device' is the number associated with the peripheral device
          and  can  be  from  1  through  255.   If device is zero (0), all
          peripherals attached will receive and act on the command sent.

               Depending on the command used with device zero, the I/O  bus
          may  become  'locked  up' with too many peripherals attempting to
          communicate at the same time.  The bus reset command,  value  255
          decimal,  may  be  specified  with  device  zero  and not cause a
          problem.  No peripherals respond with a return message  for  this
          command.

               'Command'  is a numeric code that specifies the operation to
          be performed by the device.

               'String-variable' contains  from  2  through  12  characters
          which  represent  the  data  required for the I/O operation.  The
          data passed to the  IOX  subprogram  are  interpreted  as  binary
          values.    The  'string-variable'  is  always  returned  with  12
          characters.  The data length and status  may  be  modified.   The
          format of the string is shown in the following table:

           Field          Field
           Name           Length    Description
           -------------  -------   ---------------------------------
           device           1       peripheral device code
           command          1       operation command code
           file number      1       file number as assigned in BASIC
           record number    2       record number within a file
           buffer length    2       size of the buffer for data
                                     received from the peripheral
           data length      2       number of characters to be sent
                                     to the peripheral
           status           1       status code returned by device
           buffer pointer   2       highest address of data buffer
           
          Specific  requirements for this data are given in the peripherals
          manuals.

               'Status-variable' is an optional numeric variable  in  which
          information  regarding the result of the operation is stored.  If
          no I/O error occurred, 'status-variable'  is  zero.   If  an  I/O
          error  occurred, 'status-variable' contains the corresponding I/O
          error code.  The inclusion of  a  'status-variable'  affects  the
          computer's response to the occurrence of an I/O error.  If an I/O
          error occurs when 'status-variable' is given, no error message is
          displayed  and  the  error  cannot be handled by ON ERROR.  If an
          error occurs when 'status-variable' is omitted,  the  message  is
          displayed or the error can be handled by ON ERROR.
           
          140 CALL IOX(45,1)
           
          The  above  example  closes  device 45. (A command code of 1 is a
          CLOSE operation.)