The files 'PORT2PRN.EXE' and 'PORT2PTI.EXE' are used to reset the parallel port
for use with a printer without the need to re-boot the PC.  The -PRN program
is used with IBM compatible ports, while the -2PTI program works with the
TI Professional computer.

For the IBM compatible version, specify PORT2PRN /0, PORT2PRN /1,
or PORT2PRN /2, depending on the parallel port used for the PCIF.

  /0  : primary parallel port at address 378H
  /1  : secondary parallel port at 278H
  /2  : parallel port at address 3BCH

For the TIPC version, copy the PORT2PTI.EXE file to your system for use.
No parameters are required for the TIPC version.

If this utility is not used, connecting a printer to the parallel port used for
PCIF may result in the printer being repeatedly reset due to the state of
the printer control lines.  These lines are set to a low state for use with the
PCIF, while the printer expects them to be set to a high state.  The
SAVBAT utility and PCIF set these lines low.  PORT2PRN utilities set them
high, just as if the system had been re-booted.